## Slide 1
FRANKENSTEIN FRISBEE BOT WIRING
DRIVETRAIN
LEFT 1
DRIVETRAIN
LEFT 2
SHOOTER1
DRIVETRAIN
RIGHT 1
DRIVETRAIN
RIGHT 2
SHOOTER2
Shooter Controllers MUST be set to COAST
PWMs to here
& controllers

## Slide 2
FRANKENSTEIN FRISBEE BOT PLUMBING
A
B
P
S
R
High pressure storage (120psi)
Pressure regulator
With pressure gauge
High Low  Pressure Pressure 
FIRE
FRISBEE
RAISE/LOWER
SHOOTER
Note the way this is plumbed, solenoid will extend by default. This is the fail safe state. As retracting this actuator FIRES a Frisbee.

## Slide 3
A
B
P
S
R
SOLENOID VALVE & MANIFOLD INFORMATION
Solenoid State | Port A | Port B
De-energized (OFF) | Pressurized | Vented
Energized (ON) | Vented | Pressurized
Pressure inlet
into manifold
Vented Air
Outputs
Valve Outputs To Actuators